#pragma	config OSC = HSPLL
#pragma config WDT = ON, WDTPS = 1024
#pragma config BOREN = OFF
#pragma config STVREN = ON
#pragma config LVP=OFF
#define	__MANDM_C	//	This is the main program

/*
 *
 * standard program units:
 * Voltage in (unsigned long/unsigned int) millivolts,
 * Current in (long) tenths of amps
 * Watts Power in (unsigned long)
 * Ah capacity (unsigned long) milliAh when in 32 bit variables/ (int) tenths of Ah when in 16 bit variables for net in/out Ah balance usage h[0],h[6]
 *
 * R: structure, real values from measurements
 * C: structure, calculated values from measurements or programs
 * B: structure
 *
 * USART2	is the host comm port 38400
 * Timer0	1 second clock
 * TImer1	Not used
 * Timer2	Not used
 * Timer3	work thread , background I/O clock ~20HZ
 * TImer4	PWM Period clock

 * 0..11 analog channels are active
 * PORTA	analog inputs
 * adc0	systemvoltage	PIC Controller supply voltage
 * adc1	motorvoltage
 * adc2	current_x
 * adc3	current_y
 * adc4	current_z
 * PORTB	HID Qencoder and switch inputs
 * PORTC	HID leds
 * PORTD	switch input
 * PORTE	motor control relays
 * PORTF	analog inputs
 * adc5	rawp1 X pot
 * adc6 rawp2 Y pot
 * adc7 rawp3 Z pot
 * adc8 thermo_batt	thermistor input 10K at 25C RF4
 * adc10 Ground REF	zero adc charge cap
 * adc_cal[11-14]	current sensors zero offset stored in eeprom 10=a50, 11=a50c, 12=a300, 14=future
 * cal table with checksum as last data item in adc_cal[]
 * PORTH0	run flasher led onboard, 4x20 LCD status panel
 * PORTJ	alarm and diag leds
 * PORTG
 *
 *
 * frederick.brooks@microchip.com Copyright 2012
 * Microchip Gresham, Oregon
 */

/*
 *
 * This application is designed for use with the
 * ET-BASE PIC8722 board, 4*20 LCD display
 *
 * RS-232 host commands 38400baud 8n1
 * A	send controller/battery status
 * B	select battery for modify commands, used with S M L
 * C	(NOT DONE YET)
 * D	Calibrate ADC voltages.
 * E	When in FAIL-SAVE mode switch to second battery
 * F	Force current (none critical) charge routine to exit
 * H	Dump all SD card data records to comm1 port
 * h	Dump last 1000 SD card data records to comm2 port
 * K	lockup controller causing WDT timer to reboot
 * S M L	modify selected battery type, example: ZBBMZ would set battery 2 to M type.
 * T	Tweak setting for active battery on charger
 * V	turn external charger on
 * v	turn external charger off
 * Z	reset command parser
 * ?	Send help menu to rs-232 terminal
 * $	fuse blown error. (NOT DONE YET)
 * ^	reset current sensor zero calibration
 * !	hold program in present date
 * *	set battery on CC to 100% SOC
 * #	display run data on terminal rs-232 port
 * @	display model data on terminal rs-232 port
 * P	SIMULATE PV power on
 * p	SIMULATE PV power off
 * O	SIMULATE PWM 33%
 * o	SIMULATE PWM off
 *
 */

//	***
// 0.1 mandm software.

//	***
// dipswitch settings PORTD
// 1 on=reset battery charging counters and flags
// 2 on=2 batteries/off=4 batteries to monitor
// 3 on=Force inverter to primary battery in software
// 4 on=turn on external charge power when needed
// 5 on=Learn BATTERY MODEL DATA from real data
// 6 on=FAIL-SAFE MODE, just connect C40 to PRIMARY BATTERY
// 7 on=disenable DIVERSION control of excess power when battery on charger is full
// 8 on=Force DIVERSION on
//	***

#include <p18cxxx.h>
#include <delays.h>
#include <string.h>
#include <stdlib.h>
#include <stdio.h>
#include <math.h>

#include "mandm_defs.h"
#include "xlcd.h"
#include "config.h"
#include "mandm.h"
#include "crit.h"
#include "mandm_msg.h"
#include "hwconf.h"
#include "power.h"
#include "model.h"
#include "mandm_vector.h"
#include "mandm_shared.h"
#include "daq.h"

void clr_lcd(void);
char *ahfp(long, char *);
char *voltfp(unsigned long, char *);
char *voltfps(unsigned long, char *);
char *voltfpi(long, char *);
void MputsXLCD(char *);

void fail_safe(void);
char *hms(unsigned long);
char *hm(unsigned long);
float lp_filter(float, int, int);

void putc2(unsigned char c);

void set_tweak(void); // tweak run time parameters
void hold_process(void); // hold monitor progrsm
void system_data(void); // send system variables to rs-232 terminal
void system_help(void); // send system help menu to rs-232 terminal
void display_system(void); // send adc values to terminal
unsigned char check_alarm(unsigned char, const rom char*);
long ABSL(long);
int ABSI(int);
void LCD_VC_puts(unsigned char, unsigned char, unsigned char);
void wdttime(unsigned long);
BYTE checktime(unsigned long, BYTE);
void wdtdelay(unsigned long);
void update_hist(void);
void term_time(void);

// section just for the large arrays idata
#pragma	idata	bigdata
far char bootstr2[MESG_W + 1] = {0};
unsigned char csd[SD_18] = {0}, cid[SD_18] = {0}, HCRIT[CRIT_8] = {0}, LCRIT[CRIT_8] = {0};
char p1[C_TEMP16] = {0}, p2[C_TEMP16] = {0};
char termstr[32] = {0};
far char f1[C_TEMP7] = {0}, f2[C_TEMP7] = {0}, f3[C_TEMP7] = {0}, f4[C_TEMP7] = {0};
char p3[C_TEMP16] = {0};
volatile struct almbuffertype alarm_buffer[MAXALM] = {0};
float smooth[LPCHANC] = {0};
struct lcdb ds[VS_SLOTS] = "mandm", ms[VS_SLOTS] = "mandm"; // LCD/MENU display strings, name
far char hms_string[16] = {0};

#pragma idata gpr13

int a50 = 0, a300 = 0, a50c = 0, a10_x = 0, a10_y = 0, a10_z = 0, worktick = 0, cef = 0, cef_calc = 0, cef_save = 0;
volatile unsigned char BATTNUM = MAXBATT, BCHECK = TRUE, TIMERFLAG = FALSE, PRIPOWEROK = TRUE, FORCEOUT = FALSE, workerflag = FALSE, critc_level = 0, KEYNUM = 0, b_read = 0,
CHARGEROVERRIDE = FALSE, FAILSAFE = FALSE, MORNING_HELP = FALSE, SYSTEM_STABLE = FALSE, HOLD_PROC = FALSE, C2RAW = 0, glitch_count = 0, POWER_UNSTABLE = FALSE, SET_BATT = FALSE,
fast_ticks = FT20, real_ticks = 0, BLANK_LCD = FALSE, XON_XOFF = FALSE, STATIC_SOC = TRUE, DISPLAY_MODE = FALSE, D_UPDATE = TRUE, GLITCH_CHECK = TRUE, FORCEDAY = FALSE, COOLING = FALSE,
UPDATE_EEP = FALSE, RESET_ZEROS = FALSE, SYNC_SOC = FALSE, SYNCSOC = FALSE, SYS_DATA = FALSE, MOD_DATA = FALSE, SYS_HELP = FALSE, SET_ADC = FALSE, SET_CEF = TRUE,
WDT_TO = FALSE, EEP_ER = FALSE, PERKOSW_r = FALSE, TWEAK = FALSE, cdelay = 0, SIM_MODE = RUNSIM, SIM_FLAG = 0;
volatile struct almtype alarm_codes = {FALSE, 0};
volatile unsigned char almctr = 0;
union Timers hirez_0 = 0, hirez_1 = 0;
volatile unsigned long display_count = 0,
highint_count = 0, timerint_count = 0, c1rx_int = 0, c1tx_int = 0, c2_int = 0, lowint_count = 0, status_count = 0, cctimer = 0,
pwm4int_count = 0, buttonint_count = 0, dayclockup = 0, dayclockdown = 0, worker_count = 0, clock50 = 0, critc_count = 0, d_on = 0, d_off = 0,
c_on = 0, c_off = 0, mbmcdata_count = 0, eeprom_count = 0, adc_count = 0;

#pragma idata gpr3
volatile BYTE HOST_BUSY = FALSE, HOST_COMM = FALSE, move_mode = TRUE;
volatile struct buttontype button = {0};

char sign = ' ';
float lp_speed = 0.0, lp_x = 0.0;

#pragma idata gpr15
struct R_data R = {0};
struct C_data C = {0};
const rom char *build_date = __DATE__, *build_time = __TIME__;
volatile unsigned int solarup_delay = 0;
volatile unsigned long utctime = 0;
volatile struct knobtype knob1, knob2;
volatile struct motortype motordata[4], *motor_ptr;

volatile union {
    unsigned long netdword;
    BYTE netdbyte[4];
} netd;
volatile long time_skew_base = 0, time_skew = 0;
volatile unsigned char dsi = 0, msi = 0; // LCD display string index to console 0
#pragma idata gpr4
float t1 = 0.0, t2 = 0.0, t3 = 0.0, t4 = 0.0, t5 = 0.0, t6 = 0.0, t7 = 0.0, t_time = 0.0;
#pragma idata gpr0
volatile int tx_tmp = 0, rx_tmp = 0;
volatile DWORD mbmc_cmd_reply = 0;
float voltfrak = 0.0;
float ahfrak = 0.0;
volatile long ahi_tmp = 0, aho_tmp = 0, ahop_tmp = 0;
BYTE model_update = MODEL_UPDATE;
unsigned long Vin = 0, rawp1 = 0, rawp2 = 0, rawp3 = 0, chrg_v = 0, vbatol_t = 0, solar_t = 0;
volatile unsigned char idleflag = FALSE,knob_to_pot=XAXIS;
long iw = 0, ip = 0;

#pragma idata
volatile unsigned char UTC_flag = 0, UTC_ok = 0;
volatile struct ccstype CCS = {0};
volatile unsigned int hirez_count[7] = {0, 0, 0, 0, 0, 0, 0};
/* ADC voltage/current default calibration values , adjusted with D command */
// adc_cal[11-14]	current sensors zero offset stored in eeprom 11=x, 12=y, 13=z, 14=future
unsigned char adc_cal[] = {127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 127, 0};
unsigned char CRITC = 0, LCD_OK = FALSE;

volatile enum ccmode_t {
    IDLE_M, BULK_M, FLOAT_M, TEST_M, ABSORP_M, FLOAT_W
} CCMODE;

volatile enum mbmode_t {
    IDLE_M, CHARGE_M, FLOAT_M, TEST_M
} BMMODE;

volatile enum answer_t {
    WAIT_M, YES_M, NO_M
} YNKEY;

/* ISR vectors */
#pragma code tick_interrupt = HIGH_VECTOR

void tick_int(void)
{
    _asm goto tick_handler _endasm // high
}
#pragma code

#pragma code work_interrupt = LOW_VECTOR

void work_int(void)
{
    _asm goto work_handler _endasm // low
}
#pragma code

void LCD_VC_puts(unsigned char console, unsigned char line, unsigned char COPY) // VCx,DSx, [TRUE..FALSE} copy data from bootstr2 string
{ // into the LCD display buffer
    static unsigned char ib = 0;

    if (!LCD_OK) return;
    if (COPY) {
ib = console + line; // set to string index to store data in LCD message array ds[x].b
strncpypgm2ram(ds[ib].b, " ", LCD_W); // write 20 space chars
strncpy(ds[ib].b, bootstr2, LCD_W); // move data from static buffer in lcd message array
ds[ib].b[LCD_W] = NULL0; // make sure we have a string terminator
    }

    switch (line) {
    case DS0:
SetDDRamAddr(LL1); // move to line
break;
    case DS1:
SetDDRamAddr(LL2); // move to line
break;
    case DS2:
SetDDRamAddr(LL3); // move to line
break;
    case DS3:
SetDDRamAddr(LL4); // move to line
break;
    default:
SetDDRamAddr(LL1); // move to line 1 of out of range
break;
    }
    ib = dsi + line; // set to string index to display on LCD, dsi is the current VC being displayed

    if (!D_UPDATE) return;
    if (BLANK_LCD) clr_lcd();
    while (BusyXLCD());
    putsXLCD(ds[ib].b);
    while (BusyXLCD());
}

void update_hist(void) // compute the runtime data from current data
{
    if (!SYSTEM_STABLE) return;
    check_alarm(CCS.boc, " update_hist1 ");
    // check FLAGS from the tick ISR and run subroutine if needed
    if (RESET_ZEROS) { // sero the current sensors
zero_amploc();
RESET_ZEROS = FALSE;
    }
    if (SET_ADC) { // Set gains for ADC channel calibration
set_adc_gain();
SET_ADC = FALSE;
    }
    if (TWEAK) { // Adjust runtime data
set_tweak();
TWEAK = FALSE;
    }
    if (HOLD_PROC) { // Hold processing, mainly used during a battery EQ cycle.
hold_process();
HOLD_PROC = FALSE;
    }
    if (SYS_DATA) { // display System data on rs-232 port
system_data();
SYS_DATA = FALSE;
    }
    if (SYS_HELP) { // Command Help message
system_help();
SYS_HELP = FALSE;
    }
}

void wdtdelay(unsigned long delay)
{
    static unsigned long int dcount;
    for (dcount = 0; dcount <= delay; dcount++) { // delay a bit
Nop();
ClrWdt(); // reset the WDT timer
    };
}

void wdttime(unsigned long delay) // delay = ~ .1 seconds
{
    static unsigned long dcount, timetemp, clocks_hz;
    s_crit(HL);
    clocks_hz = delay * 2; // number of low int clock ticks per second is about 20
    dcount = clock50;
    e_crit();
    clocks_hz += dcount;

    do { // wait until delay
s_crit(HL);
timetemp = clock50;
e_crit();
ClrWdt();
LCD_VC_puts(dsi, DS0, NO);
LCD_VC_puts(dsi, DS1, NO);
LCD_VC_puts(dsi, DS2, NO);
LCD_VC_puts(dsi, DS3, NO);
idle_loop();
    } while (timetemp < clocks_hz);
}

BYTE checktime(unsigned long delay, BYTE set) // delay = ~ .05 seconds
{
    static unsigned long dcount, timetemp, clocks_hz;

    if (set) {
s_crit(HL);
clocks_hz = delay; // number of low int clock ticks per second is about 20
dcount = clock50;
e_crit();
clocks_hz += dcount;
    }

    s_crit(HL);
    timetemp = clock50;
    e_crit();
    if (timetemp < clocks_hz) return FALSE;
    return TRUE;
}

void DelayFor18TCY(void)
{
    static unsigned char n;
    for (n = 0; n < 24; n++) Nop(); // works at 200
}

//------------------------------------------

void DelayPORXLCD(void) // works with 15
{
    Delay10KTCYx(15); // Delay of 15ms
    return;
}

//------------------------------------------

void DelayXLCD(void) // works with 5
{
    Delay10KTCYx(5); // Delay of 5ms
    return;
}

void putc2(unsigned char c)
{
    while (Busy2USART()) {
    }; // wait until the usart is clear
    putc2USART(c);
}

void start_delay(void)
{
    wdttime(BATRUNF); // wait for .5 seconds.
}

void clr_lcd()
{
    if (!D_UPDATE) return;
    while (BusyXLCD());
}

/*	lp_filters
0
1
2
3	current
4	currentin
5	currentcharger
6
7
8
 *	9
 */
float lp_filter(float new, int bn, int slow) // low pass filter, slow rate of change for new, LPCHANC channels, slow/fast select (1) to zero channel
{
    // smooth,lp_speed,lp_x is a udata global array to save stack space

    if (bn > LPCHANC)
return new;
    if (slow) {
lp_speed = 0.06;
    } else {
lp_speed = 0.125;
    }
    lp_x = ((smooth[bn]*100.0) + (((new * 100.0)-(smooth[bn]*100.0)) * lp_speed)) / 100.0;
    smooth[bn] = lp_x;
    if (slow == (-1)) { // reset and return zero
lp_x = 0.0;
smooth[bn] = 0.0;
    }
    return lp_x;
}

void term_time(void) // sent internal time to rs-232 terminal
{
    ClrWdt(); // reset the WDT timer
    sprintf(termstr, " CT-%s", hms(timerint_count));
    puts2USART(termstr);
    sprintf(termstr, " CU-%s", hms(dayclockup));
    puts2USART(termstr);
    sprintf(termstr, " CD-%s", hms(dayclockdown));
    puts2USART(termstr);
}

void hold_process(void) // hold the monitor in the current status until released.
{
    term_time();
    putrs2USART(hold0);
    YNKEY = WAIT_M;
    while (YNKEY == WAIT_M) {
wdtdelay(10);
ADC_read();
idle_loop();
    }
    if (YNKEY == NO_M) {
term_time();
putrs2USART(hold1);
return;
    }
    term_time();
    putrs2USART(hold1);
}

void system_data(void) // display system data on terminal
{
    ClrWdt(); // reset the WDT timer
    sprintf(bootstr2, "\r\n");
    puts2USART(bootstr2);
    term_time();
    if (SIM_MODE) {
putrs2USART(SIMULA);
    }
    putrs2USART(" FW ");
    strcpypgm2ram(bootstr2, build_time);
    puts2USART(bootstr2);
    putrs2USART(" ");
    strcpypgm2ram(bootstr2, build_date);
    puts2USART(bootstr2);
    strcpypgm2ram(bootstr2, MANDM_VERSION);
    puts2USART(bootstr2);
    sprintf(bootstr2,
   "\r\n Power status 1=OK %u, Config DIPSW %u%u%u%u%u%u%u%u, Temp Sensor %lu,Temp Comp %i\r\n Highint %lu, Lowint %lu, Timerint %lu, Workerint %lu, \r\n Com1rx int %lu, Com1tx int %lu, Com2int %lu, Bint %lu, PWMint %lu, Eint %lu, Aint %lu, Lowclocks %lu, Lowruns/S %lu,\r\n",
   PRIPOWEROK, DIPSW1, DIPSW2, DIPSW3, DIPSW4, DIPSW5, DIPSW6, DIPSW7, DIPSW8, R.thermo_batt, C.temp_drate,
   highint_count, lowint_count, timerint_count, worker_count, c1rx_int, c1tx_int, c2_int,
   buttonint_count, pwm4int_count, eeprom_count, adc_count, clock50, clock50 / timerint_count);
    puts2USART(bootstr2);
    ClrWdt(); // reset the WDT timer
}

void system_help(void) // display system help on terminal
{
    putrs2USART(keycmds0);
    putrs2USART(keycmds1);
}

void display_system(void)
{
    sprintf(bootstr2, "\n\r 0: %u,%lu Controller voltage.", adc_cal[0], R.systemvoltage);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 1: %u,%lu PV Charge Controller output voltage.", adc_cal[1], R.ccvoltage);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 2: %u,%li PV input current. Raw ADC %i", adc_cal[2], R.currentin, a50);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 3: %u,%lu PV input voltage.", adc_cal[3], R.inputvoltage);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 4: %u,%lu Battery 1 voltage.", adc_cal[4], R.primarypower[B1]);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 5: %u,%li Inverter current. Raw ADC %i", adc_cal[5], R.current, a300);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 6: %u,%lu Battery 2 voltage.", adc_cal[6], R.primarypower[B2]);
    puts2USART(bootstr2);
    //	sprintf(bootstr2, "\n\r 7: %u,%lu Not Used.", adc_cal[7], 0);
    puts2USART(bootstr2);
    // sprintf(bootstr2, "\n\r 8: %u,%li Mains charger current. Raw ADC %i", adc_cal[8], R.currentcharger, a50c);
    puts2USART(bootstr2);
}

void set_tweak(void) // modify active charge parameters
{
    int t_value, t_boc, t_more = 0;
    long t_temp, t_tempo;
    unsigned long t_keytime, t_keytime_next;
    unsigned char t_index, t_prev = 0, t_fast = FALSE;

    sprintf(bootstr2, "\r\n Tweaking Battery %i.\r\n", t_boc);
    puts2USART(bootstr2);
    C2RAW = 0;
    YNKEY = WAIT_M;
    KEYNUM = 0;
    putrs2USART(tweak0);
    while ((YNKEY == WAIT_M) && (KEYNUM == NULL0)) {
idle_loop();
    }
    if (YNKEY != WAIT_M) {
putrs2USART(tweak2);
return;
    }

    t_index = (unsigned char) KEYNUM - (unsigned char) 0x30; // convert to binary number
    if (t_index > MAX_TWEAK_CMD) {
putrs2USART(tweak2);
return;
    }

    YNKEY = WAIT_M;
    t_value = 0;
    t_keytime_next = 0;
    t_prev = 0xff;

    while (YNKEY == WAIT_M) { // display current status of parameter selected
switch (t_index) {
case 1:
   //	t_tempo = hist[t_boc].ahir;
   sprintf(bootstr2, tweak_t1);
   break;
case 2:
   //	t_tempo = hist[t_boc].ahi;
   sprintf(bootstr2, tweak_t2);
   break;
case 3:
   //	t_tempo = hist[t_boc].aho;
   sprintf(bootstr2, tweak_t3);
   break;
case 4:
   //	t_tempo = hist[t_boc].ahop;
   sprintf(bootstr2, tweak_t4);
   break;
default:
   t_tempo = 0;
   sprintf(bootstr2, tweak_tw);
   break;
}
sprintf(bootstr2, " Selected parameter #%u for adjustment on Battery %i. %s = %li\r\n", t_index, t_boc, bootstr2, t_tempo);
puts2USART(bootstr2);

if ((t_keytime_next < 3)) { // 10 fast key presses switches to high value mode
   if (C2RAW == t_prev) t_more++;
   if (t_more > 9) {
t_fast = TRUE;
putrs2USART(tweak5);
   }
} else {
   t_fast = FALSE;
   t_more = 0;
   putrs2USART(tweak3);
}

YNKEY = WAIT_M;
C2RAW = 0;
s_crit(HL);
t_keytime = timerint_count; // waiting for keypress start time
e_crit();
while (C2RAW == NULL0) {
   idle_loop();
}
s_crit(HL);
t_keytime_next = timerint_count - t_keytime; // time it took to press key (t_keytime_next-t_keytime)
e_crit();

if (YNKEY == NO_M) {
   putrs2USART(tweak2);
   return;
}
if ((C2RAW == 'Q') || (C2RAW == 'q')) {
   putrs2USART(tweak2);
   return;
}

if (t_fast) {
   if (C2RAW == 'M') t_value += 1000;
   if (C2RAW == 'L') t_value += -1000;
   if (C2RAW == 'm') t_value += 50;
   if (C2RAW == 'l') t_value += -50;
} else {
   if (C2RAW == 'M') t_value += 100;
   if (C2RAW == 'L') t_value += -100;
   if (C2RAW == 'm') t_value += 5;
   if (C2RAW == 'l') t_value += -5;
}
t_prev = C2RAW;
switch (t_index) { // make temp value with updates
case 1:
   //	t_temp = hist[t_boc].ahir + t_value;
   break;
case 2:
   //	t_temp = hist[t_boc].ahi + t_value;
   break;
case 3:
   //	t_temp = hist[t_boc].aho + t_value;
   break;
case 4:
   //	t_temp = hist[t_boc].ahop + t_value;
   break;
default:
   t_temp = 0;
   break;
}
sprintf(bootstr2, " Adjustment value %i, Parameter %s will be %li when saved.\r\n", t_value, bootstr2, t_temp);
puts2USART(bootstr2);
    }

    putrs2USART(tweak4);
    switch (t_index) { // save updated value
    case 1:
//	hist[t_boc].ahir += t_value;
break;
    case 2:
//	hist[t_boc].ahi += t_value;
break;
    case 3:
//	hist[t_boc].aho += t_value;
break;
    case 4:
//	hist[t_boc].ahop += t_value;
break;
    default:
break;
    }
    update_hist();
    putrs2USART(tweak1);
}

char* hms(unsigned long sec) // convert long (seconds) to time string
{
    static unsigned long h = 0, m = 0, s = 0;

    if (sec > MAXSECONDS) sec = MAXSECONDS; // max time in seconds
    s = sec;
    h = (s / 3600);
    s = s - (h * 3600);
    m = (s / 60);
    s = s - (m * 60);
    sprintf(hms_string, "%01lu:%02lu:%02lu", h, m, s);
    return hms_string;
}

char* hm(unsigned long sec) // convert long (seconds) to time string
{
    static unsigned long h = 0, m = 0, s = 0;
    if (sec > MAXSECONDS) sec = MAXSECONDS; // max time in seconds
    s = sec;
    h = (s / 3600);
    s = s - (h * 3600);
    m = (s / 60);
    s = s - (m * 60);
    sprintf(hms_string, "%01lu:%02lu", h, m);
    return hms_string;
}

int ABSI(int i)
{
    if (i < 0)
return -i;
    else
return i;
}

long ABSL(long i)
{
    if (i < 0)
return -i;
    else
return i;
}

char* voltfp(unsigned long millvolts, char *strprt) // convert unsigned long (millvolts) to voltage string
{
    voltfrak = (float) millvolts / 1000;
    iw = (long) ((float) voltfrak);
    ip = (long) ((float) voltfrak * 100) - iw * 100;
    sprintf(strprt, "%d.%02d", (int) iw, (int) ip);
    return strprt;
}

char* voltfps(unsigned long millvolts, char *strprt) // convert unsigned long (millvolts) to voltage string (short)
{
    voltfrak = (float) millvolts / 1000;
    iw = (long) ((float) voltfrak);
    ip = (long) ((float) voltfrak * 10) - iw * 10;
    sprintf(strprt, "%d.%01d", (int) iw, (int) ip);
    return strprt;
}

char* voltfpi(long millvolts, char *strprt) // convert long (mill volts/watts/current) to string (integer with Kilo)
{
    sign = ' '; // init sign
    if (millvolts < 0)
sign = '-';
    voltfrak = (float) millvolts / 1000;
    iw = (long) ((float) voltfrak);
    ip = (long) ((float) voltfrak * 10) - iw * 10;
    if (ABSL(iw) < 1500) {
sprintf(strprt, "%c%li", sign, ABSL(iw));
    } else {
voltfrak = voltfrak / 1000;
iw = (long) ((float) voltfrak);
ip = (long) ((float) voltfrak * 100) - iw * 100;
sprintf(strprt, "%c%li.%02lik", sign, ABSL(iw), ABSL(ip));
    }
    return strprt;
}

char* ahfp(long millah, char *strprt) // convert long (.1 of Ah) to Ah string
{
    sign = ' '; // init sign
    if (millah < 0)
sign = '-';
    ahfrak = (float) millah / 10;
    iw = (long) ((float) ahfrak);
    ip = (long) ((float) ahfrak * 10) - iw * 10;
    sprintf(strprt, "%c%d.%01d", sign, ABSI(iw), ABSI(ip));
    return strprt;
}

void battalarm(int time, int battno, int mode)
{
    ALARMOUT = R_ON;
}

//FIXME fix check_alarm

/* prints messages from the alarm array, need a rework as it's buggy */
unsigned char check_alarm(unsigned char bn, const rom char* where) // print alarm codes to terminal or just the battery number with code 251
{ // or set flag with code 253 or clear flag code 252
    static unsigned char i = 0, alm_num = 255; // if bn is 255 return state of alarm_codes.alm_flag flag TRUE/FALSE, 254 return current alarm code
    s_crit(HL);

    if (bn > 250) {
if (bn == 255) {
   if (alarm_codes.alm_flag) {
e_crit();
return TRUE;
   } else {
e_crit();
return FALSE;
   }
}
if (bn == 254) {
   e_crit();
   return alarm_buffer[almctr].alm_num;
}
if (bn == 253) {
   alarm_codes.alm_flag = TRUE;
   e_crit();
   return 253;
}
if (bn == 252) {
   alarm_codes.alm_flag = FALSE;
   e_crit();
   return 252;
}
if (bn == 251) {
   alarm_codes.alm_flag = FALSE;
   e_crit();
   return alarm_buffer[almctr].bn;
}
    }

    if (alarm_codes.alm_flag == NULL0) { // nothing, lets go
e_crit();
return FALSE;
    }

    while (almctr > NULL0) {
alm_num = alarm_buffer[--almctr].alm_num; // move down the alarm stack
term_time();
putrs2USART(where);
sprintf(bootstr2, " Q%u, Battery %u,", almctr, alarm_buffer[almctr].bn); // use the message battery number if set
puts2USART(bootstr2);
i = 0; // set alarm index to zero
if (alm_num == i++) putrs2USART(almcode0); //0
if (alm_num == i++) putrs2USART(almcode1); //1
if (alm_num == i++) putrs2USART(almcode2); //2
if (alm_num == i++) putrs2USART(almcode3); //3
if (alm_num == i++) putrs2USART(almcode4); //4
if (alm_num == i++) putrs2USART(almcode5); //5
if (alm_num == i++) putrs2USART(almcode6); //6
if (alm_num == i++) putrs2USART(almcode7); //7
if (alm_num == i++) putrs2USART(almcode8); //8
if (alm_num == i++) putrs2USART(almcode9); //9
if (alm_num == i++) putrs2USART(divert0); //10
if (alm_num == i++) putrs2USART(divert1); //11
if (alm_num == i++) putrs2USART(battbuffer0); //12
if (alm_num == i++) putrs2USART(almcode10); //13
if (alm_num == i++) putrs2USART(almcode11); //14
if (alm_num == i++) putrs2USART(almcode12); //15
if (alm_num == i++) putrs2USART(almcode13); //16
if (alm_num == i++) putrs2USART(almcode14); //17
if (alm_num == i++) putrs2USART(almcode15); //18
if (alm_num == i++) putrs2USART(almcode16); //19
if (alm_num == i++) putrs2USART(charger2); //20
if (alm_num == i++) putrs2USART(charger3); //21
if (alm_num == i++) putrs2USART(charger4); //22
if (alm_num == i++) putrs2USART(almcode17); //23
if ((alm_num > i) && (alm_num < 250)) { // if greater than last defined alarm code
   sprintf(bootstr2, " UNKNOWN Alarm code %u \r\n", alm_num);
   puts2USART(bootstr2);
}
if (almctr == NULL0) {
   alarm_codes.alm_flag = FALSE;
}
alarm_buffer[almctr].bn = 0; // set default battery number to zero
    };
    e_crit();
    return NULL0;
}

void fail_safe(void)
{
    FAILSAFE = TRUE;

    while (DIPSW6 == HIGH) { // wait until switch is clear
ADC_read();
sprintf(bootstr2, "FS T%s,SV%lu ", hms(timerint_count), R.systemvoltage / 100);
LCD_VC_puts(VC0, DS0, YES);

//	sprintf(bootstr2, "PV%lu,PI%li,CV%lu ", R.inputvoltage / 100, R.currentin / 10, R.ccvoltage / 100);
LCD_VC_puts(VC0, DS1, YES);

//	sprintf(bootstr2, "B1V%lu,B2V%lu,LI%li ", R.primarypower[B1] / 100, R.primarypower[B2] / 100, C.currentload / 10);
LCD_VC_puts(VC0, DS2, YES);

sprintf(bootstr2, "%lu, %lu, %lu ", timerint_count, clock50, clock50 / timerint_count);
LCD_VC_puts(VC0, DS3, YES);

wdtdelay(5000);
idle_loop();
    }
    FAILSAFE = FALSE;
    s_crit(HL);
    c_off = timerint_count;
    e_crit();

    alarm_buffer[almctr].bn = CCS.boc;
    alarm_buffer[almctr++].alm_num = 3;
    alarm_codes.alm_flag = TRUE;
    check_alarm(CCS.boi, " fail1 "); // send alarm codes to terminal if alm_flag is set
}

void ansidraw(int mode) // tek 410x/ansi drawing stuff
{
    putc2(ESC);
    putc2('['); // clear screen
    putc2('2');
    putc2('J');
    if (SIM_MODE) putrs2USART(SIMULA);
    putrs2USART(hello1);
    putrs2USART(hello0);
}

void update_lcd_menu(BYTE menu_text_pos)
{
    strncpypgm2ram(bootstr2, menutext + (5 + (menu_text_pos * 5)), LCD_W);
    LCD_VC_puts(dsi, DS0, YES);
    LCD_VC_puts(dsi, DS1, NO);
    LCD_VC_puts(dsi, DS2, NO);
    LCD_VC_puts(dsi, DS3, NO);
}

BYTE get_hid(void) // move_mode is global
{
    static BYTE menu_pos = 0;

    if (button.B0) {
term_time();
sprintf(bootstr2, " menu_pos %u ", (int) menu_pos);
puts2USART(bootstr2);
putrs2USART("\x1b[7m Mode Button 1. \x1b[0m\r\n");
move_mode = !move_mode; // switch modes with button 1 presses
button.B0 = FALSE;
    } else {
if (knob1.movement != STOP) { // do we have knob motion
   if (checktime(MENU_ACTION, FALSE)) { // is knob still moving and not stopped
if ((knob1.movement == CW) && (knob1.band > MENU_BAND)) { // turning clockwise
   menu_pos++;
   checktime(MENU_ACTION, TRUE); // reset the movement timer
   if (menu_pos >= MAX_MENU) menu_pos = 0;
   term_time();
   sprintf(bootstr2, " menu_pos %u ", (int) menu_pos);
   puts2USART(bootstr2);
   putrs2USART("\x1b[7m Menu Right. \x1b[0m\r\n");
} else { // CCW
   if (ABSL(knob1.band) > MENU_BAND) { // turning counter-clockwise
menu_pos--;
checktime(MENU_ACTION, TRUE); // reset the movement timer
if (menu_pos >= MAX_MENU) menu_pos = MAX_MENU;
term_time();
sprintf(bootstr2, " menu_pos %u ", (int) menu_pos);
puts2USART(bootstr2);
putrs2USART("\x1b[7m Menu Left. \x1b[0m\r\n");
   }
}
   }
} else {
   checktime(MENU_ACTION, TRUE); // reset the movement timer
}
    }
    if (move_mode) {
LED_0 = ON; // update mode led
    } else {
LED_0 = OFF; // update mode led
    }
    return menu_pos;
}

BYTE nav_menu(void)
{

}

void hid_menu(void)
{
    BYTE menu_pos;
    menu_pos = get_hid();
    update_lcd_menu(menu_pos);
    nav_menu();
}

void main(void) // Lets Party
{
    static unsigned long test_count = 0;
    static unsigned char eep_char = NULL0;
    static unsigned char z = 0;

#ifdef	__18F8722
    config_pic(PIC_8722); // configure all controller hardware to the correct settings and ports
#endif

    sprintf(bootstr2, "********************"); // blank display data
    LCD_VC_puts(VC0, DS0, YES);
    LCD_VC_puts(VC0, DS1, YES);
    LCD_VC_puts(VC0, DS2, YES);
    LCD_VC_puts(VC0, DS3, YES);

#ifdef	__18F8722
    start_pic(PIC_8722); // configure external hardware to the correct startup conditions
#endif

    wdtdelay(10000); // delay for power related LCD setup glitch
    if (BusyXLCD()) {
OpenXLCD(FOUR_BIT & LINES_5X7);
while (BusyXLCD());
wdtdelay(10000); // delay for power related LCD setup glitch
OpenXLCD(FOUR_BIT & LINES_5X7);
while (BusyXLCD());
WriteCmdXLCD(0xc); // blink, cursor off
while (BusyXLCD());
WriteCmdXLCD(0x1); // clear screen
wdtdelay(10000);
while (BusyXLCD());
LCD_OK = TRUE;
    }

#ifdef	__18F8722
    if (STKPTRbits.STKFUL) {
STKPTRbits.STKFUL = 0;
putrs2USART("\r\n");
term_time();
putrs2USART("\x1b[7m Restart from Stack Full. \x1b[0m\r\n");
    }
    if (STKPTRbits.STKUNF) {
STKPTRbits.STKUNF = 0;
putrs2USART("\r\n");
term_time();
putrs2USART("\x1b[7m Restart from Stack Underflow. \x1b[0m\r\n");
    }
#endif

    if (WDT_TO) {
putrs2USART("\r\n");
term_time();
putrs2USART("\x1b[7m Restart from Watchdog Timer. \x1b[0m\r\n");
    }

    if (EEP_ER) {
putrs2USART("\r\n");
term_time();
putrs2USART("\x1b[7m Possible EEPROM write error. \x1b[0m\r\n");
    }

    strncpypgm2ram(bootstr2, START1, LCD_W);
    LCD_VC_puts(VC0, DS0, YES);

    putrs2USART(" FW ");
    strncpypgm2ram(bootstr2, build_time, LCD_W);
    LCD_VC_puts(VC0, DS1, YES);
    puts2USART(bootstr2);
    putrs2USART(" ");

    strncpypgm2ram(bootstr2, build_date, LCD_W);
    puts2USART(bootstr2);
    LCD_VC_puts(VC0, DS2, YES);

    strncpypgm2ram(bootstr2, MANDM_VERSION, LCD_W);
    puts2USART(bootstr2);
    putrs2USART("\r\n");
    LCD_VC_puts(VC0, DS3, YES);

    // leds from outputs to ground via resistor.

    term_time();
    putrs2USART(" Configure operational data \r\n");

    if (DIPSW1 == HIGH) { // clear battery data
term_time();
putrs2USART(" Init Controller Data \r\n");
write_data_eeprom(0, 1, 0, 0); // data, number of data slots, postion, offset from eeprom address 0

term_time();
putrs2USART(" Init ADC Cal EEPROM Data \r\n");
for (z = 0; z < ADC_SLOTS; z++) {
   write_data_eeprom(ADC_NULL, ADC_SLOTS, z, 8); // data, number of data slots, postion, offset from eeprom address 0
}
    }

    term_time();
    putrs2USART(" Read Controller eeprom data \r\n");
    if (read_data_eeprom(0, 0) == CHECKMARK) { // load Controller types from EEPROM
eep_char = read_data_eeprom(2, 0);
    } else {
term_time();
putrs2USART(" Invalid Controller eeprom data \r\n"); // init eeprom data
write_data_eeprom(0, 1, 0, 0); // data, number of data slots, postion, offset from eeprom address 0
term_time();
putrs2USART(" Controller eeprom data saved\r\n"); // init eeprom data
    }

    term_time();
    putrs2USART(" Read ADC eeprom data \r\n");
    if (read_data_eeprom(0, 8) == CHECKMARK) { // load ADC cal data from EEPROM
for (z = 0; z < ADC_SLOTS; z++) {
   adc_cal[z] = read_data_eeprom(10, z);
}
    } else {
term_time();
putrs2USART(" Invalid ADC eeprom data \r\n"); // init eeprom data
for (z = 0; z < ADC_SLOTS; z++) {
   write_data_eeprom(adc_cal[z], ADC_SLOTS, z, 8);
}
term_time();
putrs2USART(" ADC eeprom data saved\r\n"); // init eeprom data
    }

    if (DIPSW6 == HIGH) { // failsafe mode
fail_safe();
while (TRUE); // Don't continue
    }

    zero_amploc(); // zero input current sensor
    term_time();
    putrs2USART(" Read ADC data inputs \r\n");
    wdttime(BATRUNF);
    ADC_read();

    if (DIPSW1 == HIGH) { // set default hist and SD data
term_time();
putrs2USART(" Init History Data \r\n");
    }

    voltfps(R.systemvoltage, f1);
    voltfps(R.motorvoltage, f2);
    sprintf(bootstr2, "Sys %sV,Mot %sV ", f1, f2); // display battery ,PV info
    LCD_VC_puts(VC0, DS0, YES);

    sprintf(bootstr2, "DIPSW %i%i%i%i%i%i%i%i ", DIPSW1, DIPSW2,
   DIPSW3, DIPSW4, DIPSW5, DIPSW6, DIPSW7, DIPSW8);
    LCD_VC_puts(VC0, DS1, YES);

    start_delay();

    wdttime(BATRUNF); // read battery and charging system voltages
    ADC_read();
    srand((unsigned int) R.systemvoltage); // set random seed

    /* Work thread start */
    start_workerthread();

    // test data
    for (z = 0; z < 3; z++) {
motordata[z].type = VIISION_M;
motordata[z].run = TRUE;
motordata[z].cw = TRUE;
motordata[z].axis = z;
motordata[z].free = TRUE;
motordata[z].slow = FALSE;
    }

    z = 1;
    // LATE = ~z;
    SYSTEM_STABLE = TRUE;
    voltfps(R.systemvoltage, f1);
    voltfps(R.motorvoltage, f2);
    sprintf(bootstr2, "S%sV,M%sV,Q%5li %5li ", f1, f2, knob1.c, knob2.c);
    LCD_VC_puts(VC0, DS0, YES);
    start_delay();
    wdttime(BATRUNF);

    /* Loop forever */
    while (TRUE) {
ADC_read();
hid_menu();

//	LCD_VC_puts(VC0, DS0, YES);
sprintf(bootstr2, "X P%2i S%2i I%3li V%3li ", motordata[0].pot.scaled_actual, motordata[0].pot.scaled_set, R.current_x, R.pos_x);
LCD_VC_puts(VC0, DS1, YES);
sprintf(bootstr2, "Y P%2i S%2i I%3li V%3li ", motordata[1].pot.scaled_actual, motordata[1].pot.scaled_set, R.current_y, R.pos_y);
LCD_VC_puts(VC0, DS2, YES);
sprintf(bootstr2, "Z P%2i S%2i I%3li V%3li ", motordata[2].pot.scaled_actual, motordata[2].pot.scaled_set, R.current_z, R.pos_z);
LCD_VC_puts(VC0, DS3, YES);
if (test_count++ >= 200ul + (knob1.c / 10)+(knob2.c / 10)) {
   if (z == 0b0000010) {
z = 1;
motordata[0].run = TRUE;
motordata[0].cw = TRUE;
motor_control(&motordata[0]);
motordata[1].run = FALSE;
motordata[1].cw = FALSE;
motor_control(&motordata[1]);
motordata[2].run = TRUE;
motordata[2].cw = TRUE;
motor_control(&motordata[2]);
putrs2USART(" motor_control test 1 \r\n");
   } else {
z = z << 1;
motordata[0].run = FALSE;
motordata[0].cw = FALSE;
motor_control(&motordata[0]);
motordata[1].run = TRUE;
motordata[1].cw = TRUE;
motor_control(&motordata[1]);
motordata[2].run = FALSE;
motordata[2].cw = FALSE;
motor_control(&motordata[2]);
putrs2USART(" motor_control test 2 \r\n");
   }
   //	LATE = ~z;
   test_count = 0;
   ADC_read();
   voltfps(R.systemvoltage, f1);
   voltfps(R.motorvoltage, f2);
   sprintf(bootstr2, "Sys %sV,Mot %sV\r\n", f1, f2);
   puts2USART(bootstr2);
   sprintf(bootstr2, "QEnc C: %5li %5li Last C: %5li %5li Band: %5li %5li\r\n", knob1.c, knob2.c, knob1.last_c, knob2.last_c, knob1.band, knob2.band);
   puts2USART(bootstr2);
   sprintf(bootstr2, "Current: X%3li Y%3li Z%3li Raw: ADC X%3i Y%3i Z%3i\r\n", R.current_x, R.current_y, R.current_z, a10_x, a10_y, a10_z);
   puts2USART(bootstr2);
   sprintf(bootstr2, "Position ADC: X%3li Y%3li Z%3li\r\n", R.pos_x, R.pos_y, R.pos_z);
   puts2USART(bootstr2);
   sprintf(bootstr2, "Pot: Xa%3i Xs%3i Ya%3i Ys%3i Za%3i Zs%3i\r\n",
   motordata[0].pot.scaled_actual, motordata[0].pot.scaled_set,
   motordata[1].pot.scaled_actual, motordata[1].pot.scaled_set,
   motordata[2].pot.scaled_actual, motordata[2].pot.scaled_set);
   puts2USART(bootstr2);
}
ClrWdt(); // reset the WDT timer
update_hist();
    }
}
/* High and Low ISR codes, some glue routines */
#include "mandm_vector.h"

#pragma	tmpdata	ISRHtmpdata
#pragma interrupt tick_handler nosave=section (".tmpdata")

void tick_handler(void) // This is the high priority ISR routine
{
    static unsigned char c1, c2;
    static unsigned char ZAP = FALSE, vc_count = NULL0;
    static unsigned char worker_timer = WORKSEC;
    static unsigned int hirez_tmp0 = NULL0, hirez_tmp1 = NULL0;
    static union Timers timer;

    static struct QuadEncoderType OldEncoder;

    _asm nop _endasm // asm code to disable compiler optimizations
   highint_count++; // high int counter
    hirez_tmp0 = (unsigned int) TMR0L;
    hirez_tmp0 += (unsigned int) (TMR0H << SHIFT8); // load high byte in tmp counter

    if (PIR2bits.EEIF) { // EEPROM write complete flag
eeprom_count++; // just keep count
MPULED = !MPULED; // flash led
PIR2bits.EEIF = LOW;
    }

    if (PIE1bits.ADIE && PIR1bits.ADIF) { // ADC conversion complete flag
adc_count++; // just keep count
//	TIMESIG=R_OFF;	// set output bit to zero
PIR1bits.ADIF = LOW;
    }

    if (INTCONbits.TMR0IF) { // check timer0 irq 1 second timer int handler
//check for TMR0 overflow
INTCONbits.TMR0IF = LOW; //clear interrupt flag
/*	reset the profile counts */
hirez_count[0] = hirez_count[2]; // copy high int counts into save var
hirez_count[2] = NULL0; // zero high int counts
hirez_count[1] = hirez_count[3]; // copy low int counts into save var
hirez_count[3] = NULL0; // zero low int counts
hirez_count[4] = hirez_count[5]; // copy low int counts into save var
hirez_count[5] = NULL0; // zero low int counts

timer.lt = TIMEROFFSET; // Copy timer value into union
TMR0H = timer.bt[HIGH]; // Write high byte to Timer0
TMR0L = timer.bt[LOW]; // Write low byte to Timer0

hirez_tmp0 = (unsigned int) TMR0L; // reload the profile start var count
hirez_tmp0 += (unsigned int) (TMR0H << SHIFT8); // load high byte in tmp counter

TIMERFLAG = TRUE;
if (fast_ticks > 10) fast_ticks = real_ticks; // measure low ints per second
real_ticks = NULL0; // reset low int counter
PIR2bits.TMR3IF = LOW; // clear possible timer3 int flag
timer.lt = TIMER3REG; // Save the 16-bit value in local, reset fast counter reg to sync
TMR3H = timer.bt[HIGH]; // Write high byte to Timer3 High byte
TMR3L = timer.bt[LOW]; // Write low byte to Timer3 Low byte

MPULED = !MPULED; // flash led
timerint_count++; // set 1 second clock counter.

display_count++; // display VC screen display timer
if (display_count > DISPSEC) { // turn off LCD after DISPSEC seconds
   //	D_UPDATE=FALSE;
}

/* cycled LCD display screens */
if (worker_timer-- <= 1) { // check worker thread go flag
   workerflag = TRUE;

   worker_timer = WORKSEC;

   if (DISPLAY_MODE) {
vc_count++;
if (vc_count >= VC_MAX) vc_count = NULL0;
switch (vc_count) {
case VS0:
   dsi = VC0;
   break;
case VS1:
   dsi = VC1;
   break;
case VS2:
   dsi = VC2;
   break;
default:
   dsi = VC0;
   break;
}
   }
}

    }

    // Serial port communications to the host and terminal
    //

    /* Get the character received from the USART */
    if (PIR1bits.RC1IF) { // is data from network port
c1rx_int++; // total count
rx_tmp++; // count for 1 second
if (RCSTA1bits.OERR) {
   RCSTA1bits.CREN = LOW; // clear overrun
   RCSTA1bits.CREN = HIGH; // re-enable
}

/* clear com1 interrupt flag */
// a read clears the flag
c1 = RCREG1; // read data from port1 and clear PIR1bits.RC1IF
    }

    /* User terminal comm routines */
    if (PIR3bits.RC2IF) { // is data from user command/dump terminal port
/* clear com2 interrupt flag */
// a read clears the flag
c2_int++;
if (RCSTA2bits.OERR) {
   RCSTA2bits.CREN = LOW; // clear overrun
   RCSTA2bits.CREN = HIGH; // re-enable
}

c2 = RCREG2; // read from host port2 and clear PIR3bits.RC2IF
C2RAW = c2; // set terminal input char.

if (c2 == 'F') { // set charge break flag
   FORCEOUT = TRUE;
}
if (c2 == '?') { // Set boc to 100% SOC
   SYS_HELP = TRUE;
}
if (c2 == '*') { // Set boc to 100% SOC
   SYNC_SOC = TRUE;
}
if (c2 == '#') { // Display system data on rs-232 terminal
   SYS_DATA = TRUE;
}
if (c2 == '@') { // Display system data on rs-232 terminal
   MOD_DATA = TRUE;
}
if (c2 == '!') { // Hold monitor processing
   HOLD_PROC = TRUE;
}
if (c2 == '^') { // set AMPLOC sensor zero flag
   RESET_ZEROS = TRUE;
}
if (c2 == 'D') { // set ADC gain flag
   SET_ADC = TRUE;
}
if (c2 == 'T') { // Tweak charge run parameters
   TWEAK = TRUE;
}
if ((c2 == 'Y') || (c2 == 'y')) { // set key flag
   YNKEY = YES_M;
}
if ((c2 == 'N') || (c2 == 'n')) { // set key flag
   YNKEY = NO_M;
}
if ((c2 >= 0x30) && (c2 <= 0x39)) { // return number
   KEYNUM = c2;
}

if (c2 == 'V') { // turn external charger on
   c_on = timerint_count;

   alarm_buffer[almctr].bn = CCS.boc;
   alarm_buffer[almctr++].alm_num = 15;
   alarm_codes.alm_flag = TRUE;
   CCS.alert = FALSE;
}
if (c2 == 'v') { // turn external charger off
   c_off = timerint_count;

   alarm_buffer[almctr].bn = CCS.boc;
   alarm_buffer[almctr++].alm_num = 14;
   alarm_codes.alm_flag = TRUE;

   CCS.alert = FALSE;
}
if (c2 == 'K') { // lockup controller in loop force WDT timeout
   while (TRUE);
}

if (c2 == 'P') { // SIM "PV voltage on"
   SIM_FLAG = 0b00000001;
}

if (c2 == 'p') { // SIM "PV voltage off"
   SIM_FLAG = 0b00000010;
}

if (c2 == 'O') { // SIM ""
   SIM_FLAG = 0b00000100;
}

if (c2 == 'o') { // SIM ""
   SIM_FLAG = 0b00001000;
}

if (c2 == 'Z' || ZAP) { // clear command flags
   ZAP = FALSE;
}
    };

    /* Control button routines */
    if (INTCONbits.INT0IF) {
DLED_0 = ON;
button.B0 = 1;
INTCONbits.INT0IF = LOW;
    }

    if (INTCON3bits.INT1IF) {
DLED_1 = ON;
button.B1 = 1;
INTCON3bits.INT1IF = LOW;
    }

    if (INTCON3bits.INT2IF) {
DLED_2 = ON;
button.B2 = 1;
INTCON3bits.INT2IF = LOW;
    }

    if (INTCON3bits.INT3IF) {
DLED_3 = ON;
button.B3 = 1;
INTCON3bits.INT3IF = LOW;
    }

    if (INTCONbits.RBIF) { // PORT B int handler for Qencoder inputs A/B
b_read = EXTIO;
buttonint_count++;
D_UPDATE = TRUE;
display_count = NULL0;
LATJ = LATJ | 0b00001111; // clear diag 0..3 leds on PORTJ

// modified version from www.piclist.com qenc-dk.htm
if (OldEncoder.OldPortB[0] != (OldEncoder.byTemp[0] = (b_read & QENC1BITS))) { // read encoder 1
   OldEncoder.OldPortB[0] = OldEncoder.byTemp[0];
   if (ENC_A1 == OldEncoder.A1) {
if (ENC_B1 == ENC_A1) {
   ++knob1.c;
   knob1.ticks = 0;
   knob1.cw = TRUE;
   knob1.ccw = FALSE;
   knob1.movement = CW;
} else {
   --knob1.c;
   knob1.ticks = 0;
   knob1.cw = FALSE;
   knob1.ccw = TRUE;
   knob1.movement = CCW;
}
   } else {
OldEncoder.A1 = ENC_A1;
if (ENC_B1 == ENC_A1) {
   --knob1.c;
   knob1.ticks = 0;
} else {
   ++knob1.c;
   knob1.ticks = 0;
}
   }
}

if (OldEncoder.OldPortB[1] != (OldEncoder.byTemp[1] = (b_read & QENC2BITS))) { // read encoder 2
   OldEncoder.OldPortB[1] = OldEncoder.byTemp[1];
   if (ENC_A2 == OldEncoder.A2) {
if (ENC_B2 == ENC_A2) {
   ++knob2.c;
   knob2.ticks = 0;
   knob2.cw = TRUE;
   knob2.ccw = FALSE;
   knob2.movement = CW;
} else {
   --knob2.c;
   knob2.ticks = 0;
   knob2.cw = FALSE;
   knob2.ccw = TRUE;
   knob2.movement = CCW;
}
   } else {
OldEncoder.A2 = ENC_A2;
if (ENC_B2 == ENC_A2) {
   --knob2.c;
   knob2.ticks = 0;
} else {
   ++knob2.c;
   knob2.ticks = 0;
}
   }
}

if (knob1.cw) {
   LED_4 = 1;
   LED_5 = 0;
}
if (knob1.ccw) {
   LED_4 = 0;
   LED_5 = 1;
}

if (knob2.cw) {
   LED_6 = 1;
   LED_7 = 0;
}
if (knob2.ccw) {
   LED_6 = 0;
   LED_7 = 1;
}

INTCONbits.RBIF = LOW;
    }
    // PWM4 ISR routines, ONLY FOR TESTING
    if (PIE3bits.TMR4IE && PIR3bits.TMR4IF) { // PWM4 post int
/* clear timer4 interrupt flag */
PIR3bits.TMR4IF = LOW;
pwm4int_count++;
    }

    hirez_tmp1 = (unsigned int) TMR0L;
    hirez_tmp1 += (unsigned int) (TMR0H << SHIFT8); // load high byte in tmp counter
    hirez_count[2] += (hirez_tmp1 - hirez_tmp0); // how many counts we were in routines
}
#pragma	tmpdata

#pragma	tmpdata	ISRLtmpdata
#pragma interruptlow work_handler nosave=section (".tmpdata")

void work_handler(void) // This is the low priority ISR routine, the high ISR routine will be called during this code section
{
    static unsigned int hirez_tmp0 = 0, hirez_tmp1 = 0;
    static union Timers timer;
    static BYTE Hsave;

    _asm nop _endasm // asm code to disable compiler optimizations
   //
   //FIXME testing ISR
   hirez_tmp0 = (unsigned int) TMR0L;
    hirez_tmp0 += (unsigned int) (TMR0H << SHIFT8); // load high byte in tmp counter
    lowint_count++; // low int trigger entropy counter
    if ((lowint_count % 200) == NULL0) MPULED = !MPULED; // flash led

    if (PIR2bits.TMR3IF) { // Timer3 int handler
timer.lt = TIMER3REG; // Save the 16-bit value in local
TMR3H = timer.bt[HIGH]; // Write high byte to Timer3 High byte
TMR3L = timer.bt[LOW]; // Write low byte to Timer3 Low byte
clock50++;
real_ticks++;

Hsave = INTCONbits.GIEH; // make a critical section
INTCONbits.GIEH = LOW;
if (++knob1.ticks >= KNOBTICKS) { // check for stopped encoders
   knob1.movement = STOP;
   knob1.ticks = KNOBTICKS;
   knob1.last_c = knob1.c; // remember where we stopped at
   knob1.band = 0;
   DLED_4 = OFF;
} else {
   knob1.band = knob1.c - knob1.last_c; // relative movement
   DLED_4 = ON;
}
if (++knob2.ticks >= KNOBTICKS) {
   knob2.movement = STOP;
   knob2.ticks = KNOBTICKS;
   knob2.last_c = knob2.c; // remember where we stopped at
   knob2.band = 0;
   DLED_5 = OFF;
} else {
   if (knob2.band != (knob2.c - knob2.last_c)) { // move pot setting with constant knob movement
motordata[knob_to_pot].pot.scaled_set += knob2.band;
   }
   knob2.band = knob2.c - knob2.last_c; // relative movement
   DLED_5 = ON;
}
INTCONbits.GIEH = Hsave; // end critical section
// constrain set limits
if (motordata[knob_to_pot].pot.scaled_set < 0) motordata[knob_to_pot].pot.scaled_set = 0;
if (motordata[knob_to_pot].pot.scaled_set > 1023) motordata[knob_to_pot].pot.scaled_set = 1023;

if (almctr > MAXALM - 2) almctr = MAXALM - 2; // check for alarm message overrun.
if (workerflag && SYSTEM_STABLE) { // WORKSEC time,
   workerflag = FALSE;
   worker_count++;
} // end of worksec functions

PIR2bits.TMR3IF = LOW; // clear int flag
    }

    hirez_tmp1 = (unsigned int) TMR0L;
    hirez_tmp1 += (unsigned int) (TMR0H << SHIFT8); // load high byte in tmp counter
    hirez_count[3] += (hirez_tmp1 - hirez_tmp0); // how many counts we were in routines
}
#pragma	tmpdata

void idle_loop(void) // idle processe to allow for better isr triggers and background networking
{

    idleflag = TRUE;
    ClrWdt();
    idleflag = FALSE;
}

void P1wait(void)
{
    while (!TXSTA1bits.TRMT) {
    };
}

void P2wait(void)
{
    while (!TXSTA2bits.TRMT) {
    };
}

/* Read analog voltage and current inputs */
#include "daq.h"

/* switch to chan 10 (shorted to ground) to reset ADC measurement cap to zero before next measurement */
void ADC_zero(void)
{
    ClrWdt(); // reset the WDT timer
    SetChanADC(ADC_CH10); // F5 grounded input
    Delay10TCYx(ADC_CHAN_DELAY);
    ConvertADC();
    while (BusyADC());
}

void ADC_read(void) // update all voltage/current readings and set load current in 'currentload' variable
{ // ADC is opened and config'd in main
    static unsigned int i; // used for fast and slow sample loops >256
    static long a10_x_t, a10_y_t, a10_z_t;

    ClrWdt(); // reset the WDT timer
    ADC_zero();
    SetChanADC(ADC_CH0); // A0 system
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    vbatol_t = Vin * (ADC0_MV - ADC_NULL + adc_cal[0]); // voltage correction factor
    vbatol_t = vbatol_t / 100;
    s_crit(HL); // turn off int
    R.systemvoltage = vbatol_t;
    e_crit();

    ADC_zero();
    SetChanADC(ADC_CH1); // A1 motor
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    solar_t = Vin * (ADC1_MV - ADC_NULL + adc_cal[1]);
    solar_t = solar_t / 100;
    s_crit(HL); // turn off int
    R.motorvoltage = solar_t;
    e_crit();

    ADC_zero();
    SetChanADC(ADC_CH2); // A2 current_x
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    a10_x = Vin; // raw ADC value

    Vin = Vin - (AMP10_ZERO - ADC_NULL + adc_cal[11]); // set zero NULL0 point
    a10_x_t = (long) Vin * (ADC2_MV - ADC_NULL + adc_cal[2]);
    if (ABSL(a10_x_t) < AMPZ)
a10_x_t = 0; // zero bit noise
    a10_x_t = (long) ((float) a10_x_t / (float) 10.0); // tenths of an amp
    a10_x_t = (long) ((float) a10_x_t / (float) AMP10_SEN);
    a10_x_t = (long) lp_filter((float) a10_x_t, LP_CURRENT_X, FALSE); // use digital filter
    if (a10_x == NULL0) a10_x_t = 0; // if sensor disconnected read zero

    ADC_zero();
    SetChanADC(ADC_CH3); // A3 current_y
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F; //
    a10_y = Vin; // raw ADC value

    Vin = Vin - (AMP10_ZERO - ADC_NULL + adc_cal[12]);
    a10_y_t = (long) Vin * (ADC3_MV - ADC_NULL + adc_cal[3]);
    if (ABSL(a10_y_t) < AMPZ)
a10_y_t = 0; // zero bit noise
    a10_y_t = (long) ((float) a10_y_t / 10.0); // tenths of an amp
    a10_y_t = (long) ((float) a10_y_t / (float) AMP10_SEN);
    a10_y_t = (long) lp_filter((float) a10_y_t, LP_CURRENT_Y, FALSE); // use digital filter
    if (a10_y == NULL0) a10_y_t = 0; // if sensor disconnected (zero) read zero current

    ADC_zero();
    SetChanADC(ADC_CH4); // A5 curent_z
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    a10_z = Vin;
    Vin = Vin - (AMP10_ZERO - ADC_NULL + adc_cal[13]); // set zero NULL0 point
    a10_z_t = Vin * (ADC4_MV - ADC_NULL + adc_cal[4]);
    if (ABSL(a10_z_t) < AMPZ)
a10_z_t = 0; // zero bit noise
    a10_z_t = a10_z_t / 10; // tenths of an amp
    a10_z_t = a10_z_t / AMP10_SEN;
    a10_z_t = (long) lp_filter((float) a10_z_t, LP_CURRENT_Z, FALSE);
    if (a10_z == NULL0) a10_z_t = 0; // if sensor disconnected read zero

    ADC_zero();
    SetChanADC(ADC_CH5); // F0 pot x
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    rawp1 = Vin;

    ADC_zero();
    SetChanADC(ADC_CH6); // F1 pot y
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    rawp2 = Vin;

    ADC_zero();
    SetChanADC(ADC_CH7); // F2 pot z
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    rawp3 = Vin;

    ADC_zero();
    SetChanADC(ADC_CH8); // F3 thermistor channel
    Delay10TCYx(ADC_CHAN_DELAY);
    Vin = 0;
    for (i = 0; i < ADC_SAMP_F; i++) {
ConvertADC();
while (BusyADC());
Vin += (unsigned int) ReadADC();
    }
    Vin /= ADC_SAMP_F;
    s_crit(HL);
    R.thermo_batt = Vin;
    R.thermo_batt -= THERMO_OFF;
    R.thermo_batt = (long) (((float) R.thermo_batt * (float) THERMO_SEN)*10.0); // tenths of C
    if ((R.thermo_batt > 1100) || (R.thermo_batt <-500)) R.thermo_batt = Temp_ZERO; // check limits 110C/-50C , default to 25C if out of limits
    R.current_z = a10_z_t;
    R.current_y = a10_y_t;
    R.current_x = a10_x_t;
    R.pos_x = rawp1;
    motordata[XAXIS].pot.scaled_actual = rawp1;
    R.pos_y = rawp2;
    motordata[YAXIS].pot.scaled_actual = rawp2;
    R.pos_z = rawp3;
    motordata[ZAXIS].pot.scaled_actual = rawp3;
    if (SIM_MODE) do_sim(); // set test data
    e_crit();
    ADC_zero(); // ground ADC input
    ClrWdt(); // reset the WDT timer
}

void do_sim(void) // create baseline test data, call in a critical section to protect from ISR updates
{
    R.thermo_batt = 250l;
    R.systemvoltage = 5000ul;
    R.motorvoltage = 24000ul;

    POWER_UNSTABLE = FALSE;
    PRIPOWEROK = TRUE;
    if (SIM_FLAG & 0b00000001) {
R.thermo_batt = 250l;
R.systemvoltage = 5000ul;
R.motorvoltage = 24000ul;
    }
    if (SIM_FLAG & 0b00000010) {
R.thermo_batt = 250l;
R.systemvoltage = 5000ul;
R.motorvoltage = 24000ul;
    }
    if (SIM_FLAG & 0b00000100);
    if (SIM_FLAG & 0b00001000);
}

void set_adc_gain(void) // set ADC gains
{
    unsigned char adc_index, z;
    ADC_read(); // update all values
    display_system();
    putrs2USART(adcg0);
    YNKEY = WAIT_M;
    KEYNUM = NULL0;
    while ((YNKEY == WAIT_M) && (KEYNUM == NULL0)) {
idle_loop();
    }
    if (YNKEY != WAIT_M) {
putrs2USART(adcg2);
return;
    }

    adc_index = (unsigned char) KEYNUM - (unsigned char) 0x30; // convert to binary number
    if (adc_index > ADC_INDEX) {
putrs2USART(adcg2);
return;
    }

    YNKEY = WAIT_M;

    while (YNKEY == WAIT_M) {
sprintf(bootstr2, "\n\r Selected ADC %u for calibration.", adc_index);
puts2USART(bootstr2);
putrs2USART(adcg3);
YNKEY = WAIT_M;
C2RAW = NULL0;
while (C2RAW == NULL0) {
   idle_loop();
}
if (YNKEY == NO_M) {
   putrs2USART(adcg2);
   return;
}
if ((C2RAW == 'Q') || (C2RAW == 'q')) {
   putrs2USART(adcg2);
   return;
}
if (C2RAW == 'M') adc_cal[adc_index] += 5;
if (C2RAW == 'L') adc_cal[adc_index] -= 5;
if (C2RAW == 'm') adc_cal[adc_index]++;
if (C2RAW == 'l') adc_cal[adc_index]--;
C2RAW = NULL0;
ADC_read(); // update all values
display_system();
    }

    putrs2USART(adcg4);
    for (z = 0; z < ADC_SLOTS; z++) {
write_data_eeprom(adc_cal[z], ADC_SLOTS, z, 8);
    }

    putrs2USART(adcg1);
}

void zero_amploc(void) // set zero current setpoint from ADC reading from a10_x a10_z a10_y, write to EEPROM
{
    unsigned char z;
    putrs2USART(zero0);
    adc_cal[11] = adc_cal[12] = adc_cal[13] = adc_cal[14] = ADC_NULL; // reset offsets to zero (ADC_NULL)
    // read adc data for zero setpoint
    ADC_read(); // a10_x=adc_[11], a10_z=adc_cal[12], a10_y=adc_cal[13]
    adc_cal[11] = (unsigned char) (ADC_NULL + (int) ((int) a10_x - (int) AMP10_ZERO));
    sprintf(bootstr2, "\n\r Zero offset %i, X current %i, AMP10_ZERO %i", (int) adc_cal[11], a10_x, AMP10_ZERO);
    puts2USART(bootstr2);

    adc_cal[12] = (unsigned char) (ADC_NULL + (int) ((int) a10_z - (int) AMP10_ZERO));
    sprintf(bootstr2, "\n\r Zero offset %i, Y current %i, AMP10_ZERO %i", (int) adc_cal[12], a10_z, AMP10_ZERO);
    puts2USART(bootstr2);

    adc_cal[13] = (unsigned char) (ADC_NULL + (int) ((int) a10_y - (int) AMP10_ZERO));
    sprintf(bootstr2, "\n\r Zero offset %i, Z current %i, AMP10_ZERO %i", (int) adc_cal[13], a10_y, AMP10_ZERO);
    puts2USART(bootstr2);

    for (z = 0; z < ADC_SLOTS; z++) {
write_data_eeprom(adc_cal[z], ADC_SLOTS, z, 8);
    }
    putrs2USART(zero1);
}

/* External device power control */
#include "power.h"

/*
 typedef struct motortype {
    BYTE type, run, cw, axis, free, slow;
} volatile motortype;
 */
int motor_control(motortype *motor)
{
    if (motor == NULL0) return (-1); // bad pointer, return error

    if (motor->type == VIISION_M) { // X/Y motors
switch (motor->axis) {
case XAXIS:
   if (motor->cw) {
emotor_cw(XD_BIT, TRUE);
   } else {
emotor_cw(XD_BIT, FALSE);
   }
   if (motor->run) {
emotor_power(XM_BIT, TRUE);
   } else {
emotor_power(XM_BIT, FALSE);
   }
   break;
case YAXIS:
   if (motor->cw) {
emotor_cw(YD_BIT, TRUE);
   } else {
emotor_cw(YD_BIT, FALSE);
   }
   if (motor->run) {
emotor_power(YM_BIT, TRUE);
   } else {
emotor_power(YM_BIT, FALSE);
   }
   break;
case ZAXIS:
   if (motor->cw) {
emotor_cw(ZD_BIT, TRUE);
   } else {
emotor_cw(ZD_BIT, FALSE);
   }
   if (motor->run) {
emotor_power(ZM_BIT, TRUE);
   } else {
emotor_power(ZM_BIT, FALSE);
   }
   break;
default:
   return (-2); // axis out of range
   break;
}
    }
    if (motor->type == E220E500_M) { // X/Y motors
    }
    if (motor->type == VHE_M) { // X/Y motors
    }
    return 0;
}

BYTE emotor_power(BYTE motor_bit, BYTE on) // select the motor power by bit position
{
    if (on) {
ERELAYS = ERELAYS&motor_bit; // and the bit low
    } else {
ERELAYS = ERELAYS | (~motor_bit); // or the bit high inverted
    }
        wdttime(RELAYRUNF); // wait for .5 seconds.
    return ERELAYS;
}

BYTE emotor_cw(BYTE motor_bit, BYTE cw) // select the motor direction by bit position
{
    if (cw) {
ERELAYS = ERELAYS | (~motor_bit); // or the bit high inverted, CW is on the NC contacts
    } else {
ERELAYS = ERELAYS&motor_bit; // and the bit low
    }
        wdttime(RELAYRUNF); // wait for .5 seconds.
    return ERELAYS;
}

#include "hwconf.h"

void config_pic(unsigned int hw_config)
{
    static char z;
    if (hw_config == 8722u) {
_asm nop _endasm // asm code to disable compiler optimizations
if (RCONbits.TO == (unsigned char) LOW) WDT_TO = TRUE;
if (EECON1bits.WRERR && (EECON1bits.EEPGD == (unsigned char) LOW)) EEP_ER = TRUE;
/* Configure all PORT pins */

ADCON1 = 0x03; // adc [0..11] enable

TRISAbits.TRISA4 = LOW; // output
TRISAbits.TRISA0 = HIGH; // an0	systemvoltage
TRISAbits.TRISA1 = HIGH; // an1 motorvoltage
TRISAbits.TRISA2 = HIGH; // an2 current_x
TRISAbits.TRISA3 = HIGH; // an3 current_y
TRISAbits.TRISA5 = HIGH; // an4 current_z

TRISB = 0x00; // all outputs first
LATB = 0xFF;
TRISBbits.TRISB0 = HIGH; //
TRISBbits.TRISB1 = HIGH; //
TRISBbits.TRISB2 = HIGH; //
TRISBbits.TRISB3 = HIGH; //
TRISBbits.TRISB4 = HIGH; // quad1 a
TRISBbits.TRISB5 = HIGH; // quad1 b
TRISBbits.TRISB6 = HIGH; // quad2 a
TRISBbits.TRISB7 = HIGH; // quad2 b
TRISC = 0x00;
LATC = 0xff;

TRISD = 0xff; // dip switch inputs

TRISE = LOW; // relay output 1
LATE = 0xff;
TRISFbits.TRISF0 = HIGH; // an5 pot_x
TRISFbits.TRISF1 = HIGH; // an6 pot_y
TRISFbits.TRISF2 = HIGH; // an7 pot_z
TRISFbits.TRISF3 = HIGH; // an8
TRISFbits.TRISF4 = HIGH; // an9
TRISFbits.TRISF5 = HIGH; // an10
TRISFbits.TRISF6 = HIGH; // an11

LATGbits.LATG3 = LOW; // output latch to zero
TRISG = 0; // tx2/rx2, pwm channels
LATG = 0xff;
TRISGbits.TRISG4 = LOW; // output for high current load relay
TRISGbits.TRISG3 = LOW; // output diversion pwm signal

TRISH = 0; // mpuled and LCD
LATH = 0xff;

TRISJ = 0; // control relays
LATJ = 0xff;

/*
* Open the USART configured as
* 9N1, 38400,38400 baud, in send and receive INT mode
*/
BAUDCON1 |= 0x08; // 16 bit mode speed register
BAUDCON2 |= 0x08; // 16 bit mode speed register

/*
* Open the USART configured as
* 8N1, 38400,38400 baud, receive INT mode
*/
Open2USART(USART_TX_INT_OFF & USART_RX_INT_ON & USART_ASYNCH_MODE & USART_EIGHT_BIT & USART_CONT_RX & USART_BRGH_LOW, 64); // 40mhz osc HS 38.4 kbaud, 16bit divider
SPBRGH2 = 0x00;
SPBRG2 = 0x40;

while (DataRdy2USART()) { // dump 2 rx data
   z = Read2USART();
};
ansidraw(TRUE); // Clear and home screen
solarup_delay = NULL;

OpenADC(ADC_FOSC_RC & ADC_RIGHT_JUST & ADC_20_TAD, ADC_CH0 & ADC_REF_VDD_VSS & ADC_INT_OFF, ADC_12ANA); // open ADC channel for current and voltage readings
PIE1bits.ADIE = LOW; // the ADC interrupt enable bit
IPR1bits.ADIP = HIGH; // ADC use high pri

OpenTimer0(TIMER_INT_ON & T0_16BIT & T0_SOURCE_INT & T0_PS_1_256);
OpenTimer3(TIMER_INT_ON & T1_16BIT_RW & T1_SOURCE_INT & T1_PS_1_8 &
T1_OSC1EN_OFF & T1_SYNC_EXT_OFF);
PR4 = 0xFF;
OpenTimer4(TIMER_INT_OFF & T4_PS_1_16 & T4_POST_1_16); // no int, only for pwm
OpenPWM4(0xFF);
T3CONbits.T3CCP1 = 1; // Bits for Timer4 for PWM
T3CONbits.T3CCP2 = 1; // same
PIE3bits.TMR4IE = LOW; // TIMER4 int enable bit
SetDCPWM4(1); // 0.1% power

INTCONbits.RBIE = HIGH; // enable PORTB interrupts 1=enable
INTCON2bits.RBIP = HIGH; // Set the PORTB interrupt-on-change as a high priority interrupt

INTCONbits.INT0IE = HIGH; //
INTCON2bits.INTEDG0 = LOW; // falling edge
INTCONbits.INT0IF = LOW; // clean possible flag

INTCON3bits.INT1IE = HIGH; //
INTCON2bits.INTEDG1 = LOW; // falling edge
INTCON3bits.INT1IF = LOW; // clean possible flag

INTCON3bits.INT2IE = HIGH; //
INTCON2bits.INTEDG2 = LOW; // falling edge
INTCON3bits.INT2IF = LOW; // clean possible flag

INTCON3bits.INT3IE = HIGH; //
INTCON2bits.INTEDG3 = LOW; // falling edge
INTCON3bits.INT3IF = LOW; // clean possible flag

z = PORTB; // dummy read to clear possible b irq
INTCONbits.RBIF = LOW; // reset B flag
INTCON2bits.RBPU = LOW; // enable input pullup. 0=on

WriteTimer0(TIMEROFFSET); // start timer0 at 1 second ticks
WriteTimer3(TIMER3REG); // low int worker thread timer about 20hz //

/* work int thread setup */
PIE2bits.TMR3IE = HIGH; // enable int
IPR2bits.TMR3IP = LOW; // make it low level

/* EEPROM write int enable */
PIE2bits.EEIE = HIGH;

/* Enable interrupt priority */
RCONbits.IPEN = HIGH;
PIR1 = LOW; // clear int flags
PIR2 = LOW;
PIR3 = LOW;

/* Make receive interrupt high priority */
IPR1bits.RC1IP = HIGH;
IPR1bits.TX1IP = HIGH;
IPR3bits.RC2IP = HIGH;

/* Enable all high/low priority interrupts */
INTCONbits.GIEH = HIGH;
INTCONbits.GIEL = HIGH;
    }
}

void start_pic(unsigned int hw_config)
{
    if (hw_config == 8722u) {
IORELAYS = 0xff; // set control relays to off at powerup/reset
    }
}

void start_workerthread(void)
{
    T2CONbits.TMR2ON = HIGH;
}

/* Switch on and off ISR enables */
#include "crit.h"

volatile void s_crit(unsigned char mode) // Start critical section of code that needs protection for the ISR
{ // remember old high and low int bits so they can be restored correctly
    static unsigned char H_tmp = 0; // keep track of time spent in critical section

    _asm nop _endasm // asm code to disable compiler optimizations
   LCRIT[CRITC] = INTCONbits.GIEL;
    if (mode & 0x2) INTCONbits.GIEL = LOW;
    HCRIT[CRITC] = INTCONbits.GIEH;
    if (mode & 0x1) INTCONbits.GIEH = LOW;
    critc_count++; // track counts
    CRITC++; // array nest level index
    if (CRITC > critc_level) critc_level = CRITC; // track nesting checking
    if ((unsigned char) CRITC == (unsigned char) CRITC1) { // only update at the first level
H_tmp = INTCONbits.GIEH;
INTCONbits.GIEH = LOW;
hirez_0.bt[LOW] = TMR0L;
hirez_0.bt[HIGH] = TMR0H; // load high byte in tmp counter
if ((unsigned char) hirez_0.lt == (unsigned char) LOW) hirez_0.lt = 0xffff; // counter overflow
INTCONbits.GIEH = H_tmp;
    }
}

volatile void e_crit(void) // End section of code that need protection from ISR
{
    static unsigned char H_tmp = 0;

    _asm nop _endasm // asm code to disable compiler optimizations
    if (CRITC) {
CRITC--;
if (!CRITC) { // only update at the first level
   H_tmp = INTCONbits.GIEH;
   INTCONbits.GIEH = LOW;
   hirez_1.bt[LOW] = TMR0L;
   hirez_1.bt[HIGH] = TMR0H; // load high byte in tmp counter
   if (!hirez_1.lt) hirez_1.lt = 0xffff; // counter overflow
   if (hirez_1.lt >= hirez_0.lt) hirez_count[5] += (hirez_1.lt - hirez_0.lt); // how many counts we were in routines
   INTCONbits.GIEH = H_tmp;
}
INTCONbits.GIEH = HCRIT[CRITC];
INTCONbits.GIEL = LCRIT[CRITC];
    } else { // default to all interrupts on with overflow
INTCONbits.GIEH = HIGH;
INTCONbits.GIEL = HIGH;
TXREG2 = '*'; // restore with no save, output to terminal port
    }
}

volatile void clear_crit(void)
{
    CRITC = NULL0;
    hirez_count[5] = NULL0;
    INTCONbits.GIEH = HIGH;
    INTCONbits.GIEL = HIGH;
}

void write_data_eeprom(unsigned char data, unsigned char count, unsigned int addr, unsigned int offset)
{

    // eeprom data array: 0=CHECKMARK checksum, 1=length of array 2=start of array data, array offset, writes must be protected from ISR
    if (addr == NULL0) { // only write header when on addr 0
s_crit(HL);
Busy_eep();
Write_b_eep(0 + offset, CHECKMARK); // write checksum at byte 0 of the offset
Busy_eep();
e_crit();
s_crit(HL);
Busy_eep();
Write_b_eep(1 + offset, count); // length of data
Busy_eep();
e_crit();
    }
    s_crit(HL);
    Busy_eep();
    Write_b_eep(addr + 2 + offset, data); // data
    Busy_eep();
    e_crit();
}

unsigned char read_data_eeprom(unsigned int addr, unsigned int offset)
{
    Busy_eep();
    return Read_b_eep(addr + offset);
}